## Slide 1: Arduino LED Blink and Button Control
Understanding Components, Wiring, and Code
https://www.tinkercad.com/

## Slide 2: Key Components
-Arduino UNO R3: the microcontroller board that runs our code.
-Breadboard: convenient board for connecting components without soldering.
-LED: emits light when current flows through it.
-Resistor: limits current to protect the LED from damage.
-Push Button: allows user input to control circuits.

## Slide 3: Task 1 – LED Blink
Goal: Make an LED blink on and off automatically.
Wiring: LED anode to pin 13, cathode through resistor to GND.
Code: Sets pin 13 as OUTPUT, turns LED HIGH and LOW with delays.
Purpose: Introduces digital output and timing with delay()

## Slide 4: Task 1 – Why We Need Each Part
Arduino UNO: provides programmable control signals.\
LED: visual indicator to show output status.
Resistor: ensures safe current for LED longevity

## Slide 6: CODE
What the code does (quick tour)
pinMode(13, OUTPUT): configures pin 13 as a digital output.
digitalWrite(13, HIGH/LOW): sets the output voltage HIGH (5V) or LOW (0V).
delay(ms): pauses the program for the given milliseconds—this creates the visible blink timing.
The loop() runs forever: ON → wait → OFF → wait → repeat.

## Slide 7: Task 2: Button Controlled Blink
Goal: LED blinks only when button is pressed.
Wiring: Button connected between pin 6 and GND
Code: Reads button state (LOW when pressed due to INPUT_PULLUP).
Behavior: LED blinks while button is pressed.

## Slide 8: Task 2 – Why We Need Each Part
Push Button: allows interactive user input.
Internal Pull-up: simplifies wiring and ensures stable signal.
Same LED & resistor: for visual feedback and protection.

## Slide 9: Code: Task 2
What the code does (quick tour)
const int ledPin = 13; const int buttonPin = 6;: names your pins for readability.
pinMode(buttonPin, INPUT_PULLUP): turns on the internal pull-up resistor.
  That means pin 6 sits at HIGH by default.
  Pressing the button connects pin 6 to GND → it reads LOW.
digitalRead(buttonPin): checks the button state each loop.
If pressed (LOW), we blink the LED with two delay(500) calls (0.5s on/off).
If not pressed, we force the LED LOW so it’s off.

## Slide 11: Learning Outcomes
Understand basic Arduino wiring and components.
"Learn digital output (LED) and input (button).
Practice coding with pinMode, digitalWrite, digitalRead, and delay.
Build foundation for more advanced interactive projects.

## Slide 12: Homework: LED Traffic Signal with Two Buttons
Create a small “traffic light” on your Arduino UNO that:
Uses three LEDs (red, yellow, green).
Has two push buttons\:
Button A starts the automatic traffic light sequence\.
Button B immediately stops the sequence and turns all lights off\.\
Цель работы: Собрать макет светофора на Arduino UNO, который:
Управляет тремя светодиодами (красный, жёлтый, зелёный). Использует две кнопки:
Кнопка A запускает автоматический цикл работы светофора.
Кнопка B немедленно останавливает цикл и выключает все лампы.
DUE: 25/09/2025